## Slide 1
Environmental Review H1 2026
Seven sites, energy, water, waste and Scope 1 + 2. Prepared for the Group Management Board.
Group Sustainability | 8 September 2026 | Factor set 2026 v1
Notes: TITLE layout. Green background, white reversed logo, Montserrat SemiBold title in white, Source Sans 3 subtitle. Taupe rule as the only accent. Keep the factor set on the title slide.

## Slide 2
SECTION 1
Where we stand after the H1 check
Intake, validation, corrections
Notes: SECTION layout. Soft Stone background, green bar on the left, small leaf-green eyebrow, green title. One line of grey context in Source Sans 3.

## Slide 3
DATA QUALITY
Three findings, three corrections, one site late
Ravensberg Consumer Brands | Group Sustainability | Internal
Page ‹#›
Paderborn reported natural gas in m³ from the new invoice format. Converted at 10.55 kWh/m³ and confirmed against the invoice kWh line.
Hameln's March electricity was exported with a wrong multiplier (ten times actual). Corrected reading supplied by the site.
Gütersloh's water was a copied monthly average. Replaced with the utility's interim statement.
Minden submitted three weeks after the deadline. Clean file.
WHAT CHANGED
Every correction is logged with source and date.
Original site files untouched.
Comparatives at the 2025 factor set.
Notes: CONTENT layout. Title in Montserrat Bold green, leaf-green underline rule. Body in Source Sans 3, 16 pt, generous spacing, max four points. Optional white card on the right with a green eyebrow for the takeaway.

## Slide 4
HEADLINE FIGURES
Group H1 2026 at a glance
Ravensberg Consumer Brands | Group Sustainability | Internal
Page ‹#›
SCOPE 1 + 2
18,299 t
-1.9% vs H1 2025
GRID ELECTRICITY
27.5 GWh
-2.6%
WATER WITHDRAWAL
506,000 m³
-1.4%
WASTE DIVERTED
98%
target 95%
FACTOR EFFECT
About 300 t of the Scope 2 reduction comes from the grid factor moving from 0.363 to 0.352 kg CO2e/kWh, not from site behaviour. Each year is calculated at its own factor set.
Notes: KPI layout. Four white tiles with a green top bar, small grey label, big green number in Montserrat Bold, one-line delta in Source Sans 3. Delta colour uses the semantic set (OK green, attention amber, problem red), never the brand green. Always add the factor-effect panel when a factor changed.

## Slide 5
EMISSIONS
Scope 1 + 2 by site, H1 2026 vs H1 2025
Ravensberg Consumer Brands | Group Sustainability | Internal
Page ‹#›
Chart: 
| Bielefeld | Bad Oeynhausen | Paderborn | Gütersloh | Hameln | Minden | Lippstadt
H1 2025 (factor set 2025) | 5153 | 684 | 5786 | 715 | 2130 | 300 | 4090
H1 2026 (factor set 2026) | 4797 | 664 | 6089 | 675 | 1970 | 289 | 3816
Notes: CHART layout. Prior period in Warm Taupe, current period in Ravensberg Green. Third series if needed: Leaf Green. Grey gridlines, no chart border, legend at the bottom, factor set named in the series label. Never colour a bar by 'good/bad' with brand greens; use the semantic set only for status marks.

## Slide 6
RATING V3
Site rating and reporting readiness
Ravensberg Consumer Brands | Group Sustainability | Internal
Page ‹#›
Site | Energy | Water | Diversion | S1+S2 | Score | Rating | Readiness
1000 Bielefeld | 19 | 19 | 25 | 19 | 82 | A | ●
1100 Bad Oeynhausen | 6 | 6 | 25 | 12 | 49 | D | ●
1200 Paderborn | 12 | 12 | 19 | 12 | 55 | C | ●
1300 Gütersloh | 12 | 19 | 25 | 19 | 75 | B | ●
1400 Hameln | 19 | 12 | 19 | 19 | 69 | B | ●
1500 Minden | 25 | 25 | 25 | 25 | 100 | A | ●
1600 Lippstadt | 12 | 12 | 25 | 19 | 68 | B | ●
Readiness: ● green passed first time, ● amber corrected after follow-up or accepted estimate, ● red missing or open. Not part of the score.
Notes: TABLE layout. Header row in Ravensberg Green with white Montserrat text, body in Source Sans 3 12 pt, zebra rows Soft Stone / white, no vertical lines. Rating letter in bold green. Readiness as a coloured dot from the semantic set, with the legend line under the table.

## Slide 7
Decisions for today
Paderborn gas: boiler assessment before the FY2026 round.
Bad Oeynhausen: warehouse template variant for H2 2026.
Approve factor set 2026 v1 for the full-year report.
Trusted brands. A more sustainable everyday.
Notes: CLOSING layout. Green background, white mark, white title, up to three decisions in Source Sans 3. Tagline in Warm Taupe at the bottom.